 Pomatsalyuk Roman HCAL_List.odt 04/12/18

HCAL Front End Electronics List

Table 1. HCAL Front End Modules List.
Module Type	Description	Inputs Channels / (Outputs)	Number / (Test Lab / +CMU)	Comments, / Power consumption / (per module)
PS776	Amplifier 10x, 16ch, / NIM	16 / (2)	18 / (14+1)	6V – 3.9W / 12V – 3.6W / Total: 7.5W
PS706	Discriminator, 16ch, / NIM	16 / (2)	19 / (18)	6V – 5.1W / 12V – 5.4W / 115V AC – 9.2W / Total: 10.5W+9.2W(AC)
Summing / Uva-120	Summing module, / 36 inputs, / NIM	36 / (1)	18 / (4+16)	6V – 4W / 12V – 4W / Total: 8W
PS740	Fan In/Out 4x4ch, / NIM	16 / (4)	5 / (2)	6V – 5.1W / 12V – 2.7W / Total: 7.8W
Summing / UVa-133 / (135)	Summing module / 4 inputs, / NIM	4x4 / (1x4)	3 / (1+1)	6V – 4W / 12V – 4W / Total: 8W
Total			63	7 NIM crates / (9 modules per crate)

Table 2. HCAL Front End Patch Panels (PP).
Patch Panel / ID	Description	Inputs Channels / (Outputs)	Number	Comments
PP1-PP5	64x BNC-BNC, / Patch Panel, size 2U	64 / (64)	5	Individual Amplitudes to / DAQ FADC
PP6-PP10	64x BNC-BNC, / Patch Panel, size 2U	64 / (64)	5	Individual Times to / DAQ TDC
SP	16x / BNC-BNC / Splitter 0.1/0.9, size 2U	16 / (16)	18	Splitter 0.1/0.9

04/12/18
Table 3. HCAL Front End Signal Cables List. (PP- patch panel)
N/n	Signal Path	Cable Type	Connectors	Number	Minimum / Length, m
1	PMT → PS776 (Ampl)	RG58	BNC-LEMO	288	6
2	PS776 → PP1-PP5	RG58	LEMO-BNC	288	2
3	PS776 → Splitter	RG58	LEMO-LEMO	288	2
4	Splitter → PS706 (Discr)	RG58	LEMO-LEMO	288	2
5	PS706 → PP6-PP10	RG58	LEMO-BNC	288	1
6	Splitter → Summing / UVA-120	RG58	LEMO-LEMO	288	2
7	Summing / UVA-120 → PS740 (Fan)	RG58	LEMO-LEMO	18	2
8	PS740→ Summing / UVA-133	RG58	LEMO-LEMO	40	1
9	Summing / UVA-133 → PS706 (Discr)	RG58	LEMO-LEMO	10	1
10	PS706 → PP10	RG58	LEMO-BNC	10	1

Table 4. Total HCAL Front End Signal Cables by Types
N/n	Connectors	Length, m / (Delay)	Total
1	BNC-LEMO	6 (30ns)	288
2	BNC-LEMO	2 (10ns)	576
3	BNC-LEMO	1 (5ns)	298
4	LEMO-LEMO	2 (10ns)	576+306=882
5	LEMO-LEMO	1 (5ns)	50

Table 5. HCAL HV Modules List.
Module Type	Description	Channels	Number / (in Test Lab)	Comments, / Power consumption / (per module)
1461N	HV module 3kV, 12ch, size 6U	12	24 / (24)	24V - 22W / Total: 22W
Total			24 / +2 spare	2 HV crates / (13 modules per crate)

Table 6. HCAL HV Cables. (PP - patch panel, HCAL-D, HV-D – distribution box)
Signal Path	Cable Type	Connectors	Number	Length (m)
PMT → HCAL-D1-24	SHV	SHV-??	288	6
HCAL-D1-24 → HV-D1-24	24 ch / SHV	??-??	12 / +1 spare	75
HV-D1-24 → HV Module	SHV	SHV-SHV	288	1